# City of Melbourne Design Standards

## Drinking fountain with dog bowl 703.02

Date issued: 07.01.2013

The drinking fountain with dog bowl is used in parks and gardens throughout the municipality. The unit comprises of the standard drinking fountain (Design Standard 703.01) with the addition of a ground level drinking bowl for pets.

These fountains are placed primarily in locations where people walk their dogs and within parks near designated dog off leash areas.

The alignment and location of drinking fountains is to be carefully considered to ensure that they are accessible from all directions and do not interfere with pedestrian circulation.

Drainage pipes should be connected to passive irrigation or water sensitive storm water systems wherever possible.

The drinking fountain is to be fabricated from grade 315 stainless steel polished to a satin finish.

### Section

### Plan

For fabrication and installation drawings refer to City of Melbourne, City Design drawings, Project No: 903457_F_DDA Drinking Fountain_Park Dog Bowl.