# City of Melbourne Design Standards

## Post and rail fence 706.01

Date issued: 07.01.2014

The post and rail fence is used to prevent vehicle access from park perimeters and around car parking areas.

Post material is to be Iron Bark or White Cypress Pine (Class A) dressed all round (DAR) 150mm square section.

Fences should be designed to suit a standard 6.5m pipe rail length. Space posts to create three equal length bays in every full length run. Provide gaps for pedestrian access, minimum 1300mm maximum 1500mm wide.

Where the fence follows a row of street trees, align with trunks and centre trees in gaps ensuring pedestrian access  provision is still retained.

For fabrication and installation drawings, refer to City of Melbourne, City Design drawings; Project No: 5015 Post and Rail Fence.

### Elevation

### Section