# City of Melbourne Design Standards

## Steel safety rail fence 706.07

Date issued: 07.01.2014

The steel safety rail fence is used in selected footpaths throughout the municipality where there is a need for a barrier to control pedestrian movement.

Examples include selected major intersections and entrances to major facilities or where there is a significant level change at the kerb line.

The safety rail fence is set back from the kerb line a minimum of 600mm.

The posts and fence panels are fabricated in mild steel and powder coated in Dulux 'Silver Glow Pearl' 84623.

For fabrication and installation details, refer to City of Melbourne, Engineering Standard Drawing. 1P 50514 Pedestrian Safety Fence (Federation Style).

### Elevation

### Plan